## Slide 1: Learning-Based Power Modeling of System-Level Black-Box IPs
Dongwook Lee, Taemin Kim, Kyungtae Han, Yatin Hoskote, Lizy K. John, Andreas Gerstlauer

## Slide 2: Source-/Transaction-Level Modeling
TLM
SW
Custom
Hardware
Legacy IPs
SW Compiler
HW Compiler
Fast functional simulation
Native host execution
Parallel system interactions
Energy
Timing
…
Static analysis
Back-annotation
Machine learning & prediction

## Slide 3: Related Work
High-level power modeling
Tradeoff between speed and accuracy
Enable fast and accurate power simulation
Functional
Model
CDFG/FSMD Model
RTL/Micro-Arch. Model
Activity-based
Power model
Coarse grained State-based
Power model
Simulation model
Power model
Accuracy
Speed
[Schürmans13,Copty11,Lee06 ]
[Micro Arch: Sunwoo11,Park09]
[RTL:Ravi03,Gupta2000]
[FSMD: Shao14]
Proposed

## Slide 4: Related Work
Learning-based white-box power modeling
  Model complexity reduction is a key concern
    Model decomposition [Lee15]
  Detailed architecture information is required
Black-box power modeling
  Lack of internal architecture information
  Mostly coarse grained state-based approaches
  Extended state-based model [Lorenz14]
    Refine state where significant power variation is observed
    Significant overhead to capture cycle-by-cycle input activity
  Proposed approach
    Transaction-level activity and advanced learning technique

## Slide 5: Outline
  Introduction
  Related Work
  Power Modeling Approach
    Cycle level vs invocation vs ensemble learning
  Power Model Synthesis
    Decomposition
  Experimental Results
  Summary and Conclusion

## Slide 6: Proposed Power Modeling Flow
TLM
Model
TB
[1,2]
[3,4]
…
Black-Box
IP Gate Module
Sim.
Gate-lv
Sim.
Transaction-Level I/O Trace
Cycle-Level Power Trace
Power Model Synthesis
Power Model
Invoc.
mW
Invoc. Power Trace
nsec
mW
Invocation-level
Data-dependent, Fast
Transaction-Level Activity
cycles
MEM
HW
1
2
3
CPU
HW_SIM()
Start
Done
1
2
3
HW_SIM()
Start
Done

## Slide 7: Power Modeling
Internal signal activity of single-cycle logic
Internal signal activity of multi-cycle logic
P(t)= F1(A1(t),A2(t),A3(t),A4(t),A5(t),A6(t),A7(t))
+
+
X
A1
A2
A3
A4
A5
A6
A7
Correlated
≅ F2(A1(t),A2(t),A3(t),A4(t),A7(t)) // Both I/O
Comb
Logic
Comb
Logic
R0
Comb
Logic
R1
AI(t)
AO(t)
P(t)= F1(AI(t),AR0(t),AR1(t), AO(t))
≅ F2(AI(t),AI(t-1),AI(t-2),
AO(t), AO(t+1), AO(t+2))
Utilize history of I/O activity

## Slide 8: Cycle-Level Power Model
TLM Simulation
Transaction-Level I/O Trace
cycles
MEM
HW
1
2
3
CPU
3
4
7
HW_SIM()
HW_SIM()
Start
Done
DOUT
DIN
CLK
1
2
3
4
3
7
0
0
Cycle-Level I/O Trace
Invoc.
Invoc.
Cycle Level I/O Trace Reconstruction
Compute Invocation Power
Invoc.
mW
Invoc. Power Trace
Pinvoc ≅ avgi(fcycle(A(ti))
Start
Done
Cycles
Cycle-Level Activity Computation
H(0,1), H(1,1), H(1,2), H(2,2), …
H(0,0), H(0,0), H(0,0), H(0,3), …
H(0,0), H(0,1), H(1,1), H(1,2), …
H(0,0), H(0,0), H(0,3), H(3,3), …
…
Ports
Cycles
Ports
Activity History
Cycle-Level I/O Activity Vector
H(0,1), H(1,1), H(1,2), H(2,2), …
H(0,0), H(0,0), H(0,0), H(0,3), …
H(0,0), H(0,1), H(1,1), H(1,2), …
H(0,0), H(0,0), H(0,3), H(3,3), …
…
Redundant & always zeros
Reduce overhead !!

## Slide 9: Invocation-Level Power Model
TLM Simulation
Transaction-Level I/O
Activity Computation
Compute Invocation Power
Transaction-Level I/O Trace
cycles
MEM
HW
1
2
3
CPU
3
4
7
HW_SIM()
HW_SIM()
Start
Done
Start
Done
Invoc.
mW
Invoc. Power Trace
Pinvoc ≅ finvoc(A(t))
H(0,1), H(2,3), H(4, 4), …
H(1,2), H(3,4), H(4, 6), …
H(0,3), H(3,7), H(7,10), …
Invocations
Transaction-Level I/O Activity Vector
Trans.
Transaction-level I/O activity vector
  Reduce overhead
Problem
  Worst case dimension
  Generalization errors

## Slide 10: Learning-Based Power Model Synthesis
Power Model Synthesis
I/O Activity
[1,0,0,…]
[1,2,2,…]
[1,2,2,…]
…
[0,0,0,…]
Feature Vector
Power
3mW
4mW
5mW
…
1mW
Gate Lv Power
Training Data
Learning
Cycle-Level
Decomposition
Power Model
  Cycle-level decomposition
    Decompose the power model based on execution latencies
    Hierarchically perform the cycle-by-cycle decomposition
  Feature selection
    Decision tree based feature selection
    Remove unused features in each decomp. model
Feature Selection

## Slide 11: Power Model Decomposition
Single power model w/ internal architecture info.
Decomposed power model for white-box IP [Lee15]
  Utilize architecture information to reduce model complexity
    Only capture signals (features) of operators utilized in each state
P1(t)= f1(Aa(t),Ab(t),Ac(t),Ad(t),Ae(t),Af(t))
P2(t)= f2(Ac(t),Ad(t),Af(t),Ag(t),Ah(t),Ai(t))
P3(t)= f3(Ag(t),Ah(t),Ai(t))
X
X
+
+
X
S1
S2
S3
P(t)= f(An(t)), n=a…i

## Slide 12: Power Model Decomposition
Single power model w/o internal architecture info.
Decomposed power model for black-box IP
X
X
+
+
X
S1
S2
S3
Cycles
P1(t)= f1(An(t), An(t-1), An(t-2)), n=a…d
P2(t)= f2(An(t), An(t-1), An(t-2)), n=a…d
P3(t)= f3(An(t), An(t-1), An(t-2)), n=a…d
a
b
c
d
P(t)= f(An(t), An(t-1), An(t-2)), n=a…d
Full history of I/O signal activities are utilized to estimate internal activities
  Only part of activities contribute to power consumption of decomp. model
  Uncertainty of each model is decreased

## Slide 13: Model Summary and Comparison
Cycle model
  Single model, different activity
  Computation overhead
Invocation model
  Single model, total activity
  Simple, but poor accuracy
Decomposed model
  Cycle-by-cycle models, total activity
  Variation of ensemble learning
  Decision tree regression is utilized
  Decision tree based feature selection is applied
Pinvoc ≅ avgi(fcycle(A(ti))
Pinvoc ≅ finvoc(A(t))
Pinvoc ≅ avgi(fS(i)(A(t))

## Slide 14: Experiments
Setup
  Machine learning [scikit-learn]
Application
Training
  Gate level power simulation: 6 ~ 20 min
  Training time: 20 ~ 120 sec
 | Gates | Total I/O Ports | I/O Delay | Exec. Cycles | Train Invoc. | Test Invoc. | Total Test Cycles
GEMM | 964 | 2/1 | 12 | 436 | 1250 | 5000 | 2.2M
DCT | 6309 | 4/4 | 64 | 96 | 2700 | 10800 | 1.0M
QUANT | 1456 | 3/1 | 4 | 410 | 10000 | 36864 | 5.0M
R2Y | 1757 | 4/1 | 6 | 806/742 | 1200 | 3600 | 2.8M
HDR Kernel | 7887 | 11/1 | 57 | 825 | 900 | 1300 | 1.1M

## Slide 15: Comparison of Power Models
Learning overhead and model accuracy comparison
  QUANT
m-L : w/ linear regression
C : Cycle model
I : Invocation model
E : Ensemble model

## Slide 16: Comparison of Learning Models
Accuracy
Simulation Speed
  Decision tree model is selected
DT: Decision Tree GB: Gradient Boost,
BR: Bayes Ridged SVR: Supporting Vector Regression w/ RBF kernel
Chart: MAE [%]
| GEMM | DCT | R2Y | QUANT | HDR
C | 0.03 | 0.021 | 0.037 | 0.068 | 0.042
I | 0.044 | 0.025 | 0.076 | 0.04 | 0.041
E-DT | 0.023 | 0.0132 | 0.0074 | 0.005 | 0.0216
E-GB | 0.023 | 0.013 | 0.0074 | 0.0063 | 0.021
E-BR | 0.023 | 0.038 | 0.0373 | 0.059 | 0.0267
E-SVR | 0.0258 | 0.0412 | 0.099 | 0.083 | 0.0588
Chart: Cycles/sec.
| GEMM | DCT | R2Y | QUANT | HDR
C | 38509.0973 | 16010.093 | 24610.0138 | 46254.9801 | 27366.6752
I | 252841.5681 | 224360.5327 | 548850.3159 | 330651.4774 | 486747.7535
E-DT | 187931.0345 | 167801.6529 | 390548.8372 | 269477.7563 | 312682.2157
E-GB | 150344.8276 | 148204.3796 | 192293.1298 | 261879.6992 | 130952.381
E-BR | 191228.0702 | 170050.2513 | 394627.6762 | 270261.8817 | 323042.1687
E-SVR | 104057.2792 | 20625.7619 | 343115.5505 | 289045.6432 | 105873.6426

## Slide 17: Overall Accuracy and Speed Result
Less than 3% MAE
Avg. 260 kcycles/s
  300x faster than gate-level
  9x faster than cycle model
Chart: MAE
| GEMM | DCT | R2Y | QUANT | HDR
C | 0.03 | 0.021 | 0.037 | 0.068 | 0.042
I | 0.044 | 0.025 | 0.076 | 0.04 | 0.041
E-DT | 0.023 | 0.014 | 0.009 | 0.005 | 0.022
Chart: Cycles/sec
| GEMM | DCT | R2Y | QUANT | HDR
C | 38500 | 16000 | 24600 | 46300 | 27400
I | 252800 | 224300 | 548800 | 330700 | 319100
E-DT | 141000 | 168000 | 378000 | 304000 | 319000
Gate | 378 | 188 | 2099 | 1518 | 876

## Slide 18: Results: Power Traces
DCT
R2Y
HDR

## Slide 19: Summary and Conclusion
Power modeling for black-box IPs
  Transaction-level I/O activity
    Enable fast simulation speed
  Power model decomposition and ensemble estimation
    Enable accurate data-dependent power prediction
  Advanced machine learning techniques
Simulation performance
  Running at average 263 kcycle/sec
  <3% invocation-by-invocation error
  <2% average error

## Slide 20: Thank you http://www.ece.utexas.edu/~gerstl

## Slide 21: Results: Power Traces (2)
GEMM
QUANT